## Slide 1
2025-05-22
Daisuke Moriyama
PRINCIPAL ENGINEER
Renesas Electronics Corporation
AST-AA-25-0025
Automotive Trends in
MCU/SoC Features:
Opportunities for Work in
GlobalPlatform

## Slide 2: Automotive in-vehicle Architecture
AST-AA-25-0025
Today - Centralized architecture
Vehicle Level
Gateway
Domain control
Simple actuator
Tomorrow - Zone architecture
Central compute/
Zone
Simple actuator
      Scalable & Easy to plug-in hardware
Upgradable & Reusable software
Safe, redundant and streamlined network

## Slide 3: Automotive MCU/SoC security development
AST-AA-25-0025
Automotive OEM and Tier1 companies
Request for Quotation
Original J3101
SESIP PP for J3101? (future)
?
?
Develop and supply MCU/SoC
Semiconductor vendors
SESIP security functional requirements
GP_FST_070

## Slide 4: Today’s talk
AST-AA-25-0025
MCU/SoC features
J3101
SESIP
Today I focus on several gaps
from viewpoint of one automotive MCU/SoC vendor

## Slide 5: Gap 1: Crypto HW/SW test after power-on
AST-AA-25-0025
Automotive MCU
HSM
CPU
Crypto HW
Application CPUs
Peripheral IPs
Flash
Boot code
App code
App data
HSM FW
Crypto lib
Power ON
Secure boot
Launch Application
Cryptographic
integrity
check
Startup flow several people imagine
RAM
RAM

## Slide 6: Gap 1: Crypto HW/SW test after power-on
AST-AA-25-0025
Automotive MCU
HSM
CPU
Application CPUs
Flash
Boot code
App code
App data
HSM FW
Crypto lib
Power ON
Secure boot
Power On Self Test (POST)
Logic BIST and Memory BIST
Launch Application
Real startup flow
Input/Output
check
Crypto HW
Peripheral IPs
RAM
RAM
Cryptographic
integrity
check

## Slide 7: Gap 1: Crypto HW/SW test after power-on
AST-AA-25-0025
Automotive MCU
HSM
CPU
Application CPUs
Flash
Boot code
App code
App data
HSM FW
Crypto lib
Crypto HW
Peripheral IPs
RAM
RAM
SESIP:
Only focus secure boot
J3101:
Require cryptographic algorithm self-test before secure boot
Its motivation will be to check crypto operation
check w/
test vector

## Slide 8: Gap 2: (Accidental) FW update failure
AST-AA-25-0025
Automotive MCU
HSM
CPU
Flash
Boot code
App code
App data
HSM FW
Crypto lib
Crypto HW
RAM
If integrity check & update are
successfully finished
No trouble
If integrity check is failed
No trouble
If integrity check is passed but overwrite process is incidentally failed
Problematic (car becomes scrap!)
Update file
Integrity OK
Accident happens
RAM

## Slide 9: Gap 2: (Accidental) FW update failure
AST-AA-25-0025
Automotive MCU
HSM
CPU
Flash
Boot code
App code
App data
HSM FW
Crypto lib
Crypto HW
RAM
Double bank mechanism is adopted
(to enhance both safety & security)
When a failure happens, next activation
is proceeded from the other bank
Boot code
App code
HSM FW
Crypto lib
bank 0
bank 1

## Slide 10: Gap 2: (Accidental) FW update failure
AST-AA-25-0025
Automotive MCU
HSM
CPU
Crypto HW
RAM
bank 0
bank 1
SESIP:
While FW update is required, no criteria
to support double bank mechanism
J3101:
Require fallback to prevent system failure
Example includes “dual memory”
architecture (as left figure)
Flash
Boot code
App code
App data
HSM FW
Crypto lib
Boot code
App code
HSM FW
Crypto lib

## Slide 11: Gap 3: How to check Application CPU
AST-AA-25-0025
Automotive MCU/SoC
HSM
CPU
Crypto HW
RAM
Crypto operation
request
Crypto operation
result
HSM must securely manage
secret keys for each application CPU
How does HSM identify application CPUs?
Application CPU 1
Application CPU 2
Application CPU n
...
APP

## Slide 12: Gap 3: How to check Application CPU
Application CPU 1
Application CPU 2
Application CPU n
...
AST-AA-25-0025
Automotive MCU/SoC
HSM
CPU
Crypto HW
RAM
Crypto operation
request
Crypto operation
result
A simple solution: Assign static ID in HW
or setup dedicated ID from HSM
The assigned ID can be transferred as a
sideband information in the system bus
No application CPU/SW cannot cheat ID!
ID config HW
write
allocate
CPU | ID
App CPU 1 | 0x02
App CPU 2 | 0x07
App CPU 3 | 0x09
APP

## Slide 13: Gap 3: How to check Application CPU
AST-AA-25-0025
Automotive MCU/SoC
HSM
CPU
Crypto HW
RAM
Crypto operation
request
Crypto operation
result
SESIP:
No focus on this issue
J3101:
Require prior authorization
before crypto operation
If J3101 follows FIPS140, this requires
- ID-password authentication or
- cryptographic authentication (MAC or signature)
Somewhat
authentication
Application CPU 1
Application CPU 2
Application CPU n
...
APP

## Slide 14: Gap 4: Performance of crypto operation
AST-AA-25-0025
V2x communication requires digital signature e.g., 1000 signatures per second
Internet communication requires encrypted data transaction (with TLS) e.g., 10Gbps for 5G network
Secure boot requires low-latency signature verification or MAC verification e.g., xxx ms until application OS starts
In-vehicle communication requires low-latency CMAC e.g., 100 us for 1 AES block
...

## Slide 15: Gap 4: Performance of crypto operation
AST-AA-25-0025
Automotive MCU/SoC
HSM
CPU
Crypto HW
RAM
AES HW
SHA2 HW
SHA3 HW
RSA/ECC HW
TRNG
Pure SW implementation
Crypto HW acceleration
100x-1000x throughput
Crypto HW support is natural
to cover many scenarios
High-throughput and latency demands are higher than typical IoT devices

## Slide 16: Gap 4: Performance of crypto operation
AST-AA-25-0025
Automotive MCU/SoC
HSM
CPU
Crypto HW
RAM
AES HW
SHA2 HW
SHA3 HW
SESIP:
No throughput criteria for crypto operation
J3101:
No throughput criteria for crypto operation
Performance criteria depends on
each use-case and OEM
RSA/ECC HW
TRNG

## Slide 17: Gap 5: debug isolation
AST-AA-25-0025
Automotive MCU/SoC
HSM
CPU
Application CPU 1
Crypto HW
RAM
Application CPU 2
Application CPU n
...
RAM
SW1 for CPU 1
SW2 for CPU 2
SWn for CPU n
HSM FW
SW1 developer
SW2 developer
SWn developer
HSM developer
Many companies involve
automotive software development

## Slide 18: Gap 5: debug isolation
AST-AA-25-0025
Automotive MCU/SoC
HSM
CPU
Application CPU 1
Crypto HW
RAM
Application CPU 2
Application CPU n
...
RAM
SW1 for CPU 1
SW2 for CPU 2
SWn for CPU n
HSM FW
Many companies involve
automotive software development
Debug access area should be isolated even in application area
ID | Area 1 | Area 2 | HSM Area
ID A | OK (after auth) | NG | NG
ID B | NG | OK (after auth) | NG
ID C | NG | NG | OK (after auth)
config

## Slide 19: Gap 5: debug isolation
AST-AA-25-0025
Automotive MCU/SoC
HSM
CPU
Application CPU 1
Crypto HW
RAM
Application CPU 2
Application CPU n
...
RAM
SW1 for CPU 1
SW2 for CPU 2
SWn for CPU n
HSM FW
SESIP:
Multiple developers are not so focused in secure debug
For in-field operation (not debug),
SESIP defines several isolations
Application
HSM1
HSM
HSM2
Application1
Application2
J3101:
Require HSM/normal debug isolation only
Application
HSM

## Slide 20: Future argument
AST-AA-25-0025
MCU/SoC features
J3101
SESIP
Several SESIP and J3101
requirements are related to
application layer security and operational issues
How to find the gap in them
may be provided by OEM/Tier1

## Slide 21: SUMMARY
Automotive MCU/SoC include practical security features
  Other semiconductor vendors may provide additional security features... please share!
I wish GlobalPlatform extracts real demands from automotive OEM/Tier1/chip vendors to establish usable certification and standardization
AST-AA-25-0025

## Slide 22
Renesas.com
AST-AA-25-0025