## Slide 1: Cybersecurity Threats and Risks; International Regulatory Developments; PQC (Post-Quantum Cryptography)
Global Technical & Cybersecurity Advisor
Dennis Kengo Oka
dennis.kengo.oka@iav.jp
GlobalPlatform Cybersecurity Vehicle Forum
May 15, 2025, Shanghai, China

## Slide 2: Introduction of IAV
26 Locations worldwide
6,600 Employees
Founded 1983 Berlin
Vehicle Solutions & Autonomous Driving
Software Systems & Connectivity
Powertrain Systems

## Slide 3: Dr. Dennis Kengo Oka
    Started working on automotive security in 2006
    Involved in standardization and best practices activities
    70+ publications and presentations at events
    Global Technical & Cybersecurity Advisor
Author of books: “Building Secure Cars: Assuring the Automotive Software Development Lifecycle” and “Building Secure Automotive IoT Applications: Developing Robust IoT Solutions for Next-Gen Automotive Software”
Notes: 1.5min

## Slide 4: Agenda
Cybersecurity Threats and Risks for SDVs
International Regulatory Developments
PQC (Post-Quantum Cryptography)
Notes: 2.5min

## Slide 5: Agenda
Cybersecurity Threats and Risks for SDVs
International Regulatory Developments
PQC (Post-Quantum Cryptography)

## Slide 6: Overview of Automotive Threats in 2024
Incidents targeting IT systems, IVI systems and ADAS were most prevalent
Ref: VicOne 2025 Automotive Cybersecurity Report VIcOne Automotive Cybersecurity Snapshot
Chart: 
| IT systems | IVI systems | ADAS | EV charging | BMS | ECU | Keyless entry | Diagnostics | Fleet management | Mobile/Vehicle apps | Other
Incidents | 28.7 | 16.7 | 14.45 | 12.55 | 7.8 | 7.35 | 5.6 | 2.75 | 1.4 | 1.35 | 1.35
ECU: Electronic Control Unit
BMS: Battery Management System
EV: Electric Vehicle
ADAS: Advanced Driver Assistance System
IVI: In-Vehicle Infotainment
Notes: 3min
https://documents.vicone.com/reports/shifting-gears-2025-automotive-cybersecurity-report.pdf
IT systems 28.7
IVI systems 16.7
ADAS 14.45
EV charging 12.55
BMS 7.8
ECU 7.35
Keyless entry 5.6
Diagnostics 2.75
Fleet management 1.4
Mobile/Vehicle apps 1.35
Other 1.35

## Slide 7: Overview of Published Automotive Vulnerabilities
Increasing number of automotive vulnerabilities published year over year
Ref: VicOne 2025 Automotive Cybersecurity Report VIcOne Automotive Cybersecurity Snapshot
Chart: 
| 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025
Vulnerabilities | 6 | 5 | 2 | 15 | 36 | 266 | 340 | 290 | 355 | 426 | 530
500+
Notes: https://documents.vicone.com/reports/shifting-gears-2025-automotive-cybersecurity-report.pdf
Total of 215 incidents

## Slide 8: SDV Ecosystem – New Use Cases and Technologies
Advanced software and increased connectivity to support new SDV use cases
Phone as a key
Smart parking
Summon vehicle
Remote diagnostics
Vehicle management
SDV: Software-Defined Vehicle
V2X: Vehicle to X
V2X
Cellular
Wi-Fi
Bluetooth
Applications
Linux/Android
AUTOSAR Adaptive
Virtual Machines
Notes: 4.5min

## Slide 9: Increased Attack Surface
Advanced software and increased connectivity lead to increased attack surface
Reverse-engineering of mobile apps
Session hijacking/Man-in-the-middle attacks
Unauthorized access to mobile app’s memory
SDV: Software-Defined Vehicle
API: Application Programming Interface
API abuse
Data leakage of vehicle/user data
Unauthorized access
Bruteforce attempts
Exploit software vulnerabilities
Replay attacks
Spoofing
Bypass/break weak authentication
Notes: 6min

## Slide 10: End-to-End Cybersecurity Solutions
End-to-end cybersecurity solutions are needed to reduce the risks
Anti reverse-engineering techniques
Secure communication and session management
Memory protection and secure storage
API: Application Programming Interface
IAM: Identity and Access Management
Secure APIs and service communication
End-to-end encryption
IAM
Logging and monitoring
Firewalls, TLS
Secure E/E arch.
SecOC
Key Management
Secure boot
SDV: Software-define vehicle
TLS: Transport Layer Security
SecOC: Secure Onboard Communication
Notes: 8.5min

## Slide 11: Secure End-to-End Lifecycle
DevSecOps – CI/CD
AI tooling
Digital Vehicle Key
Key Management
SecOC
End-to-End Encryption
Security Functions
IDS
Secure Boot
Secure Communication
Secure APIs
VSOC
OTA updates
Code Review
Functional Security Tests
Fuzz Testing
Pentesting (full vehicle/ ECU/cloud/mobile apps)
Security Testing
Security Engineering
TARA
Security Requirements
Security Concepts
Training
Best practices
CSMS
SUMS
Processes
CSMS: Cybersecurity Management System
IDS: Intrusion Detection System
TEE: Trusted Execution Environment
CI/CD: Continuous Integration/ Continuous Delivery
TARA: Threat Analysis and Risk Assessment
SecOC: Secure Onboard Communication
CSMS: Cybersecurity Management System
SUMS: Software Update Management System
VSOC: Vehicle Security Operations Center
OTA: Over the Air
ECU: Electronic Control Unit
Optimizations
Baseline
Operations
Notes: 12min

## Slide 12: Agenda
Cybersecurity Threats and Risks for SDVs
International Regulatory Developments
PQC (Post-Quantum Cryptography)
Notes: 14.5min

## Slide 13: Security Regulations Worldwide at a Glance
today
Country / Region | Regulation / Standards | Details | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029
Global | ISO/CD 24882 | Tractors and Agricultural Machinery – Cybersecurity Engineering |  |  |  |  |  |  |  | 
 | ISO/SAE 21434 | Cybersecurity for Road Vehicles |  |  |  |  |  |  |  | 
UNECE WP29 | R155 | Approval for M&N vehicle types and OEMs according ISO21434 |  |  |  |  |  |  |  | 
EU | EU Data Act | Fair access to and use of data |  |  |  |  |  |  |  | 
 | New Machinery Regulations | Industrial machinery/machinery products |  |  |  |  |  |  |  | 
 | Cyber Resilience Act (CRA) Regulation EU 2024/2847 | cybersecurity requirements for products with digital elements |  |  |  |  |  |  |  | 
 | NIS2 & RCE / CRITICAL | directives for cyber resilience of critical entities / infrastructure |  |  |  |  |  |  |  | 
United Kingdom | Product Security and Telecommunications Infrastructure Act | Radio equipment |  |  |  |  |  |  |  | 
Japan | Regulations on Terminal Equipment, etc. | Security of wireless/IoT devices |  |  |  |  |  |  |  | 
 | UNECE R155 | Approval for M&N vehicle types and OEMs with OTA-Update |  |  |  |  |  |  |  | 
 |  | Approval for M&N vehicle types and OEMs without OTA-Update |  |  |  |  |  |  |  | 
United States | U.S. Cyber Trust Mark | Security certification system for wireless devices/IoT products |  |  |  |  |  |  |  | 
China | GB 44495-2024 | Technical requirements for vehicle cybersecurity |  |  |  |  |  |  |  | 
Expected to be applicable mid 26
released 2/23
DIS 1/22
new types 7/22
all vehicles produced 7/24
in force 01/24
applicable 09/2025
partly effective 6/23
fully applicable1/27
in force 12/24
fully applicable 12/27
new types 7/22
all vehicles produced 7/24
new types 1/24
all vehicles produced 5/26
in force 4/24
law 9/23
Offical launch 01/25
new types end 25
all vehicles produced end 27
published 10/24
Expected to be in force 10/25
Report obligation 09/26
WD 4/24
CD 1/25
Notes: NT: New type approval; NV: Every new vehicle
Unece R155 for Motorcycles: https://unece.org/sites/default/files/2023-11/ECE-TRANS-WP.29-GRVA-2024-04e_0.pdf
We would like to refer to the ongoing work within ISO TC23 (agricultural vehicles/machines) SC19 (electronics) on an ISO New Work Item Proposal initiating a new standard on cybersecurity. By mid 2026, this new standard will be applicable to our industry.
https://www.cema-agri.org/images/publications/position-papers/2023_01_23_PP_on_the_CRA.pdf
Regulation (EU) 2023/1230 of the European Parliament and of the Council of 14 June 2023 on machinery replaces Directive 2006/42/EC on machinery. … The Regulation applies from 20 January 2027. However, some rules already apply on earlier dates such as the requirements for notified bodies (14 January 2024). https://osha.europa.eu/de/legislation/directive/regulation-20231230eu-machinery
CRA enters into Force 11.12.2024: https://www.bsi.bund.de/EN/Themen/Unternehmen-und-Organisationen/Informationen-und-Empfehlungen/Cyber_Resilience_Act/cyber_resilience_act_node.html
Manufacturers will have to apply the rules 36 months after their entry into force. The Commission will then periodically review the Act and report on its functioning. https://digital-strategy.ec.europa.eu/en/policies/cyber-resilience-act
Originally scheduled for enforcement in August 2024, the Radio Equipment Directive (RED) has been postponed to 2025 due to ongoing preparation of harmonized standards. Consequently, all wireless devices and products sold in the European Union (EU) will be required to comply with the RED delegated act from August 1, 2025. https://www.sgs.com/en-gb/news/2023/07/safeguards-9523-radio-equipment-directive-red-delegated-act-for-cybersecurity-officially-postponed
On Jan. 12, 2022, the Official Journal of the European Union published delegated regulation 2022/30/EU, enforcing compliance requirements to RED Article 3.3(d), (e) and (f). The regulation requires cybersecurity, personal data privacy and fraud protection for applicable wireless devices available on the EU market (see figure). It takes effect Feb. 1, 2022, and becomes mandatory Aug. 1, 2025, giving device manufacturers a 42-month transition period. https://www.ul.com/services/ul-solutions-cybersecurity-advisory-red-compliance
Product Security and Telecommunications Infrastructure Act https://www.lexology.com/library/detail.aspx?g=46f3087d-48d4-4110-81be-430142ba8b4e#:~:text=These%20regulations%20were%20signed%20into,commence%20on%2029%20April%202024
Cyber trust mark https://www.whitehouse.gov/briefing-room/statements-releases/2023/07/18/biden-harris-administration-announces-cybersecurity-labeling-program-for-smart-devices-to-protect-american-consumers/

## Slide 14: Cybersecurity – R155 vs. CRA vs. GB-44495 (1)
Topic | UN R155 | CRA | GB-44495
Products effected | Road vehicles (M, N, O (at least one ECU), L) | Products with digital elements | Road vehicles (M, N, O (at least one ECU))
Required management system | Mandates formal CSMS certification, renewal every 3 years | Approved quality system would be sufficient | Requires CSMS audit but does not issue certificate, expects renewal every 3 years
Risk assessment | Risk assessment as part of CSMS alongside with mitigation | Simple risk assessment sufficient; needs to be part of technical documentation | Requires risk assessment of threats and vulnerabilities for products and systems
Legend:
Less strict
More strict
Notes: 15min
Cars, buses, trucks, trailers, motorcycles fall under UN R155 and not CRA
L will be moved out from CRA scope on Dec 11, 2027
L for UN R155 will start from 1 July 2029

## Slide 15: Cybersecurity – R155 vs. CRA vs. GB-44495 (2)
Topic | UN R155 | CRA | GB-44495
Technical requirements | Threats and abstract countermeasures specified in Annex 5 | Essential abstract requirements are defined in Annex I | Includes specific technical controls, such as authentication protocols, intrusion detection, and data security measures
Testing and certification | CSMS & Vehicle Types needs to be tested by technical service and certified by approval authority | Depending on type of product: self-declaration, third-party conformity assessment, or European cybersecurity certification | Testing of cybersecurity functions is required based on 27 defined security tests (e.g., external interfaces, access control, communications security); third-party labs may conduct evaluations
Cryptography requirements | Does not mandate specific algorithms but expects appropriate cryptographic measures aligned with best practices | No fixed algorithms, but secure, up-to-date cryptographic standards must be used | Specifies international, national or industry standard crypto modules (e.g., Chinese cryptographic algorithms)
Legend:
Less strict
More strict
Notes: 17min
CRA:
Non-critical products -> self-assessment
Important class I -> self-assessment if apply harmoinzed standards, common specifications or European cybersecurity certification -> if not, mandatory third-party conformity assessment
Important class II -> mandatory third-party conformity assessment
Critical products -> mandatory European Common Criteria (EUCC) certification assessment by authorized confirmity assessment body
GB: testing using third-party labs
Does not specify if the labs must be accredited by national body
Compliance with GB rests with the vehicle manufacturer – they need to ensure that the testing conducted (internally or third-party) meets the standards requirements and effectively validates the cybersecurity measures implemented
Chinese crypto:
SM2: elliptic curve-based public key algorithm for digital signatures and key exchange
SM3: hash function
SM4: symmetric-key block cipher for data encryption/decryption

## Slide 16: Cybersecurity – R155 vs. CRA vs. GB-44495 (3)
Topic | UN R155 | CRA | GB-44495
Reporting obligations | OEM to report yearly new attacks and actions effectiveness of implemented mitigation / additional actions | Manufacturer to report actively exploited vulnerabilities or severe incidents to ENISA within 24 hours, and more detailed incident notification within 72 hours | Processes in place for vulnerability management but no specific reporting timelines or authorities to report to
Fixing vulnerabilities | Remediation of threats and vulnerabilities in the product within a reasonable timeframe | Manufacturers shall ensure that vulnerabilities of that product, including its components, are handled effectively | Must implement vulnerability handling processes (e.g., NVDB-CAVD); known high-risk vulnerabilities must be fixed within 6 months
Service duration | … until end-of-life of all vehicles | Support period shall be at least 5 years... If expected to be in use for longer, support period shall correspond to the expected usage time | No specific minimum update period but manufacturers are expected to maintain processes that ensure continued cybersecurity of vehicles throughout their operational life
Legend:
Less strict
More strict
Notes: 18.5min
CRA: first early warning notification to ENISA within 24 hrs, more details about affected product, nature of exploit and vulnerability, corrective or mitigating measures taken etc. within 72 hrs
UNR: end-of-life could be 10-15 yrs

## Slide 17: Agenda
Cybersecurity Threats and Risks for SDVs
International Regulatory Developments
PQC (Post-Quantum Cryptography)
Notes: 20min

## Slide 18: Future Technologies – Quantum Computing
Ref: https://content.techgig.com/technology/the-dawn-of-quantum-computing-introducing-qnodeos-the-first-quantum-operating-system/articleshow/120586133.cms https://news.microsoft.com/source/features/innovation/microsofts-majorana-1-chip-carves-new-path-for-quantum-computing/ https://www.fujitsu.com/global/about/resources/news/press-releases/2025/0422-01.html
New advancements in Quantum Computing
Notes: 20min
Majorana 1: different approach to building fault-tolerant qubits -> low error rates and high stability
Today’s superconducting and trapped ion qubits require thousands of physical qubits to make one logical qubit
-> If Majorna 1 is successful could accelerate path to practical scalable quantum computing
First quantum OS: QNodeOS
Can manage and execute applications across quantum network nodes -> facilitate scalable and functional quantum internet
256 qubit – other quantum systems have achieved higher qubit counts but
Fujitsu and riken stands out because advanced thermal design, integration between quantum computing and HPC (hybrid) and strategic roadmap for 1000 qubits
256 qubit quantum computer can represent 2^256 different quantum states simultaneously
256 qubit not powerful yet to break modern crypto
Today’s quatum computers are noisy (prone to errors) and lack error correction
To break e.g. RSA-2048, need estimated thousands to millions of logical qubits (not physical qubits but logical ones after correction)
https://news.microsoft.com/source/features/innovation/microsofts-majorana-1-chip-carves-new-path-for-quantum-computing/
Microsoft today introduced Majorana 1, the world’s first quantum chip powered by a new Topological Core architecture that it expects will realize quantum computers capable of solving meaningful, industrial-scale problems in years, not decades.
In the same way that the invention of semiconductors made today’s smartphones, computers and electronics possible, topoconductors and the new type of chip they enable offer a path to developing quantum systems that can scale to a million qubits and are capable of tackling the most complex industrial and societal problems, Microsoft said.
https://content.techgig.com/technology/the-dawn-of-quantum-computing-introducing-qnodeos-the-first-quantum-operating-system/articleshow/120586133.cms
Quantum computing advances with QNodeOS. It is the first operating system for quantum computers. It supports different quantum systems. This solves compatibility issues. QNodeOS has two parts: CNPU and QNPU. It uses NetQASM for instructions. Researchers tested it by linking quantum computers. Future plans include more tests and improvements. QNodeOS may lead to advancements in various fields.
Quantum computers don’t use standard parts. Each machine can use a different kind of qubit. Some use atoms, others use diamonds, and a few use superconductors. QNodeOS connects them all.
QNodeOS has a cool combo of two main parts: CNPU (Classical Network Processing Unit): This kicks off code execution.
QNPU (Quantum Network Processing Unit): This handles all quantum instructions.
https://www.fujitsu.com/global/about/resources/news/press-releases/2025/0422-01.html
Fujitsu Limited and RIKEN today announced the development of a world-leading 256-qubit superconducting quantum computer, established at the RIKEN RQC-FUJITSU Collaboration Center. This new quantum computer builds upon the advanced technology of the 64-qubit iteration, launched with the support of the Japanese Ministry of Education, Culture, Sports, Science and Technology (MEXT)(1) in October 2023, and incorporates newly-developed high-density implementation techniques. This announcement marks another crucial step toward the practical application of superconducting quantum computers and unlocking their potential to grapple with some of the world’s most complex issues.
Both organizations will integrate the 256-qubit superconducting quantum computer into its platform for hybrid quantum computing lineup and offer it to companies and research institutions globally starting in the first quarter of fiscal 2025. The platform's expansion from 64 to 256 qubits empowers users to tackle more complex challenges, including the analysis of larger molecules and the implementation and demonstration of sophisticated error correction algorithms.

## Slide 19: Quantum Computing Impact on Cybersecurity
Can factor large integers exponentially faster than best-known classical algorithms
Affects: Asymmetric encryption algorithms that rely on the difficulty of factoring large integers or finding discrete logarithms
Result: Big threat – e.g., RSA and ECC could be completely broken – private keys can be extracted from public keys
Can speed up bruteforce attacks (but only by a square root)
Affects: Symmetric encryption algorithms that rely on key size and infeasibility of bruteforcing all possible keys
Result: Partial threat – e.g., AES-128 would be weakened to half the security (64-bit strength)
Quantum Computing has severe impact on Cybersecurity
Shor’s algorithm
Grover’s algorithm
RSA: Rivest Shamir Adleman
ECC: Elliptic Curve Cryptography
AES: Advanced Encryption Standard
Notes: 21min

## Slide 20: PQC Approaches
Post Quantum Computing Crypto solutions are needed to address the risks
ECDH: Elliptic Curve Diffie Hellman
AES: Advanced Encryption Standard
SHA: Secure Hash Algorithm
HMAC: Hash-based Message Authentication Code
PQC: Post-Quantum Cryptography
RSA: Rivest Shamir Adleman
ECC: Elliptic Curve Cryptography
ECDSA: Elliptic Curve Digital Signing Algorithm
Traditional Algorithm | Quantum Vulnerability | PQC Approach
RSA | Broken by Shor’s algorithm | CRYSTALS-Kyber (key exchange)
ECC (ECDSA, ECDH) | Broken by Shor’s algorithm | CRYSTALS-Dilithium (signatures)
AES-128 | Grover’s algorithm halves security (64 bits) | Use AES-256
SHA-2 (SHA-256) | Grover’s algorithm halves preimage resistance (128 bits) | Continue with SHA-2 or use SHA-512 for extra margin
SHA-3-256 | Grover’s algorithm halves preimage resistance (128 bits) | Continue with SHA-3-256 or use SHA-3-512 for extra margin
HMAC | Depends on underlying hash (SHA-2 or SHA-3) | See above for SHA-2 and SHA-3-256
ChaCha20 (256 bits) | Grover’s algorithm halves security (128 bits) | Continue with ChaCha20 (256 bits)
Notes: 22.5min
Bruteforce preimage attack – generate preimage after you know the target hash
Use Grover’s algorithm to check guesses live -> classical bruteforce resistance is 2^n -> grover’s algorithm halves to 2^(n/2) operations
ChaCha20: stream cipher using 256 bit key
- Works well on resource constrained devices

## Slide 21: Crypto Agility Cryptographic algorithms can get outdated ⇒ need to be updatable
Notes: 25min

## Slide 22: Crypto Agility - IAV quantumSAR Concept
IAV quantumSAR is divided into two parts
  Post-Quantum Algorithm: platform-independent library with all algorithm standardized by NIST
    Implemented in C and RUST
    Available as open-source repository on GitHub (C available now, RUST to follow in 2025)
    Extendable design for future standardized algorithm (e.g., NIST PQC selection round 4)
  Wrapper: platform-dependent wrapper for adaption on different software architectures
    Implementation for AUTOSAR Classic Platform
NIST: National Institute of Standards and Technology
PQC: Post-Quantum Cryptography
Notes: 25.5min
Round 3: CRYSTALS-Kyber, CRYSTALS-Dilithium, Falcon, SPHINCS+
Round 4 candidates: BIKE, Classic McEliece, HQC, SIKE
HQC was selected on March 11, 2025 for standardization
SIKE was removed in 2022 due to vulnerability

## Slide 23: Crypto Agility - Firmware Security Module Securable, scalable and updatable Trusted Execution Environment
Full support of all necessary security functionalities
  Secure Boot and Secure Update
  Secure Logging
  Intrusion Handling
  Cryptographic Algorithm
    Including Post-Quantum Cryptography (PQC)
  Secure Key Management
  etc.
PQC: Post-Quantum Cryptography
Notes: 27min

## Slide 24: Crypto Agility - Firmware Security Module Securable, scalable and updatable Trusted Execution Environment
Integration approaches
  Hardware Security Module (HSM)
  Isolated Main Cores
  Isolated Virtual Machines (VM)
Combination of approaches possible
  Adaptable for different system designs
  Flexible for future extensions
HSM: Hardware Security Module
VM: Virtual Machine
Notes: 28min

## Slide 25: Call to Action
Stay up-to-date on automotive risks for the SDV ecosystem
Deploy end-to-end security solutions (vehicle, cloud, mobile device)
Apply best practices for secure end-to-end development lifecycle
Be aware of differences in regulatory requirements
Get ready for PQC
SDV: Software-Defined Vehicle
PQC: Post-Quantum Cryptography
Notes: 29.5min

## Slide 26: Contact
Dr. Dennis Kengo Oka
IAV Co., Ltd.
dennis.kengo.oka@iav.jp
www.iav.com
Notes: 30min