## Slide 1
Assessing Security Levels & Functional Interoperability
Cybersecurity Vehicle Forum
May 2025
WEI YUAN
PUBLIC
CC
CC

## Slide 2
00
03
01
Context
Attack Potential & Attack Methods
Final thoughts
02
SESIP Assurance Levels & Protection Profiles
AGENDA

## Slide 3: Context
Context
Attack Potential & Attack Methods
SESIP Assurance Levels & Protection Profiles
Final thoughts

## Slide 4
Context
00
📈 Growth of Connected Vehicles
The number of connected vehicles is rapidly increasing.
Projections indicate that over 327 million connected vehicles will be in service by 2027, encompassing advanced mobility platforms such as autonomous vehicles and electric vertical take-off and landing vehicles.
This surge significantly expands the number of vehicle endpoints exposed to potential cyberattacks.
🔓 Expanded Attack Surfaces
Modern vehicles integrate numerous electronic control units (ECUs) and communication interfaces, including Bluetooth, Wi-Fi, and cellular networks. This complexity introduces multiple potential entry points for cyberattacks.
Infotainment systems: Vulnerable to control override and injection attacks.
Telematics units: Susceptible to unauthorized remote access.
On-Board Diagnostics (OBD-II) ports: Can be exploited for direct access to vehicle networks.
Automotive Security Today
⚠️ Escalating Cybersecurity Challenges
The automotive industry faces significant cybersecurity threats, including compromised safety, privacy breaches, financial losses, and reputational damage.
Automotive cybersecurity market is projected to grow from $3.9 billion in 2023 to $5.9 billion by 2025, reflecting the industry's response to these escalating threats.

## Slide 5
Context
00
SESIP Methodology and Protection Profiles
Pragmatic (and industry friendly) view of CC
Granularity to reinforce Composition and Reusability
Compliance demonstration (with requirements mappings) against industry proposals.
ENISA's Attack Methodology
EUCC Scheme and CC evaluation methodology.
Experience in Technical Domains for SCSD and HWSB.
Set of State of the Art (SoTA) documentation.
Automotive Cybersecurity from a different view

## Slide 6
SESIP Methodology and Protection Profiles
Pragmatic (and industry friendly) view of CC
Granularity to reinforce Composition and Reusability
Compliance demonstration (with requirements mappings) against industry proposals.
Context
00
ENISA's Attack Methodology
EUCC Scheme and CC evaluation methodology.
Experience in Technical Domains for SCSD and HWSB.
Set of State of the Art (SoTA) documentation.
Automotive Cybersecurity from a different view
https://certification.enisa.europa.eu/certification-library/eucc-certification-scheme_en

## Slide 7
Context
00
SESIP Methodology and Protection Profiles
Pragmatic (and industry friendly) view of CC
Granularity to reinforce Composition and Reusability
Compliance demonstration (with requirements mappings) against industry proposals.
ENISA's Attack Methodology
EUCC Scheme and CC evaluation methodology.
Experience in Technical Domains for SCSD and HWSB.
Set of State of the Art (SoTA) documentation.
Automotive Cybersecurity from a different view

## Slide 8
Context
00
SESIP Methodology and Protection Profiles
Pragmatic (and industry friendly) view of CC
Granularity to reinforce Composition and Reusability
Compliance demonstration (with requirements mappings) against industry proposals.
ENISA's Attack Methodology
EUCC Scheme and CC evaluation methodology.
Experience in Technical Domains for SCSD and HWSB.
Set of State of the Art (SoTA) documentation.
Automotive Cybersecurity from a different view
https://www.nxp.com/company/about-nxp/smarter-world-blog/BL-SESIP-SYSTEM

## Slide 9
Context
00
SESIP Methodology and Protection Profiles
Pragmatic (and industry friendly) view of CC
Granularity to reinforce Composition and Reusability
Compliance demonstration (with requirements mappings) against industry proposals.
ENISA's Attack Methodology
EUCC Scheme and CC evaluation methodology.
Experience in Technical Domains for SCSD and HWSB.
Set of State of the Art (SoTA) documentation.
Automotive Cybersecurity from a different view
SESIP Methodology and Protection Profiles
Pragmatic (and industry friendly) view of CC
Granularity to reinforce Composition and Reusability
Compliance demonstration (with requirements mappings) against industry proposals.
https://globalplatform.org/specs-library/?filter-committee=sesip&filter-document_types=859

## Slide 10: Attack Potential & Attack Methods
Context
Attack Potential & Attack Methods
SESIP Assurance Levels & Protection Profiles
Final thoughts

## Slide 11
Applus+ experience on automotive penetration testing
Attack Potential & Attack Methods
01
Traditional pentest request:
Typically, software attacks methods in scope
Sometimes, hardware attacks methods considered in TARAs, but removed from scope
Very Limited budget without priorization of attack vectors
Fuzzing
Code Injection
Cryptographic Failures
Broken Access Control
Security Misconfiguration
Vulnerable and Outdated Components
Code Review

## Slide 12
Applus+ experience on automotive penetration testing
Attack Potential & Attack Methods
01

## Slide 13
Applus+ experience on automotive penetration testing
Attack Potential & Attack Methods
01

## Slide 14
Applus+ experience on automotive penetration testing
Attack Potential & Attack Methods
01

## Slide 15
Attack Potential & Attack Methods
01
Hardware Security Boxes and Automotive Parallels:
Hardware security boxes and ECUs share attack exposure definition.
ENISA attack potential model is mature and effective
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)

## Slide 16
Hardware Security Boxes and Automotive Parallels:
Hardware security boxes and ECUs share attack exposure definition.
ENISA attack potential model is mature and effective
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)

## Slide 17
Hardware Security Boxes and Automotive Parallels:
Hardware security boxes and ECUs share attack exposure definition.
ENISA attack potential model is mature and effective
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
Attack Potential & Attack Methods
01

## Slide 18
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
Hardware Security Boxes and Automotive Parallels:
Hardware security boxes and ECUs share attack exposure definition.
ENISA attack potential model is mature and effective
Attack Potential & Attack Methods
01

## Slide 19
Hardware Security Boxes and Automotive Parallels:
Hardware security boxes and ECUs share attack exposure definition.
ENISA attack potential model is mature and effective
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
Attack Potential & Attack Methods
01

## Slide 20
Attack potential rating example
Attack scenario:
Target:
  Bypass FW signature verification during FW update process with the target to load a forged FW with malicious code.
Identification of (potential) vulnerability:
  When wrong FW is processed, different error messages are received.
  The verification of the FW might not be protected against faults.
Attack method:
  Perturbation attack using Voltage glitch
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)

## Slide 21
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 5 | 2
Expertise | 2 | 2
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 14 | 14
 | 28 (Moderate resistance) | 

## Slide 22
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 5 | 2
Expertise | 2 | 2
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 14 | 14
 | 28 (Moderate resistance) | 

## Slide 23
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 5 | 2
Expertise | 2 | 2
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 14 | 14
 | 28 (Moderate resistance) | 

## Slide 24
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 5 | 2
Expertise | 2 | 2
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 14 | 14
 | 28 (Moderate resistance) | 

## Slide 25
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 5 | 2
Expertise | 2 | 2
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 14 | 14
 | 28 (Moderate resistance) | 

## Slide 26
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 5 | 2
Expertise | 2 | 2
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 14 | 14
 | 28 (Moderate resistance) | 

## Slide 27
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 5 | 2
Expertise | 2 | 2
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 14 | 14
 | 28 (Moderate resistance) | 

## Slide 28
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 5 | 2
Expertise | 2 | 2
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 14 | 14
 | 28 (Moderate resistance) | 

## Slide 29
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 5 | 2
Expertise | 2 | 2
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 14 | 14
 | 28 (Moderate resistance) | 

## Slide 30
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 5 | 2
Expertise | 2 | 2
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 14 | 14
 | 28 (Moderate resistance) | 

## Slide 31
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 5 | 2
Expertise | 2 | 2
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 14 | 14
 | 28 (Moderate resistance) | 

## Slide 32
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 5 | 2
Expertise | 2 | 2
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 14 | 14
 | 28 (Moderate resistance) | 

## Slide 33
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 5 | 2
Expertise | 2 | 2
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 14 | 14
 | 28 (Moderate resistance) | 

## Slide 34
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 3 | 2
Expertise | 2 | 0
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 11 | 12
 | 21 (Enhanced-Basic resistance) | 

## Slide 35
Attack potential rating example
Attack Potential & Attack Methods
01
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)
 | Identification | Exploitation
Elapsed time | 3 | 2
Expertise | 2 | 0
Knowledge of TOE | 2 | 2
Access to TOE: Samples | 2 | 4
Equipment and tools | 3 | 4
Windows of Opportunity | 0 | 0
Final table | 11 | 12
 | 21 (Enhanced-Basic resistance) | 

## Slide 36
Attack Potential & Attack Methods
01
Harmonized criteria to rate attack difficulty:
Supports layered defense strategy helping to prioritize testing investment
Easier quantification of cost of the attacks (in USD)
Promotes budget-efficiency while clarifying criteria for laboratories.
ENISA SoTA: Application of attack potential to hardware devices with security boxes (HWSB)

## Slide 37: SESIP Assurance Levels & Protection Profiles
Context
Attack Potential & Attack Methods
SESIP Assurance Levels & Protection Profiles
Final thoughts

## Slide 38
SESIP Assurance Levels & Protection Profiles
02
Objective to reduce the cost, complexity, and effort associated with security evaluations.
Emphasis on modularity and the reuse of certified components.
SESIP contribution for Automotive sector
Modular Evaluation:
Automotive systems comprise various components like ECUs, telematics units, and infotainment systems. SESIP allows for individual evaluation of these components, facilitating targeted security assessments.
Reuse of Certified Components:
Manufacturers can integrate previously certified components into new systems without re-evaluating the entire system, saving time and resources.
Support for ISO/SAE 21434 Compliance:
SESIP's methodology supports compliance with ISO/SAE 21434, the international standard for automotive cybersecurity risk management.

## Slide 39
SESIP Assurance Levels & Protection Profiles
02
SESIP contribution for Automotive sector
Modular Evaluation:
Automotive systems comprise various components like ECUs, telematics units, and infotainment systems. SESIP allows for individual evaluation of these components, facilitating targeted security assessments.

## Slide 40
SESIP Assurance Levels & Protection Profiles
02
Objective to reduce the cost, complexity, and effort associated with security evaluations.
Emphasis on modularity and the reuse of certified components.
SESIP contribution for Automotive sector
Modular Evaluation:
Automotive systems comprise various components like ECUs, telematics units, and infotainment systems. SESIP allows for individual evaluation of these components, facilitating targeted security assessments.
Reuse of Certified Components:
Manufacturers can integrate previously certified components into new systems without re-evaluating the entire system, saving time and resources.
Support for ISO/SAE 21434 Compliance:
SESIP's methodology supports compliance with ISO/SAE 21434, the international standard for automotive cybersecurity risk management.

## Slide 41
SESIP Assurance Levels & Protection Profiles
02
SESIP contribution for Automotive sector
Reuse of Certified Components:
Manufacturers can integrate previously certified components into new systems without re-evaluating the entire system, saving time and resources.

## Slide 42
SESIP Assurance Levels & Protection Profiles
02
Objective to reduce the cost, complexity, and effort associated with security evaluations.
Emphasis on modularity and the reuse of certified components.
SESIP contribution for Automotive sector
Modular Evaluation:
Automotive systems comprise various components like ECUs, telematics units, and infotainment systems. SESIP allows for individual evaluation of these components, facilitating targeted security assessments.
Reuse of Certified Components:
Manufacturers can integrate previously certified components into new systems without re-evaluating the entire system, saving time and resources.
Support for ISO/SAE 21434 Compliance:
SESIP's methodology supports compliance with ISO/SAE 21434, the international standard for automotive cybersecurity risk management.

## Slide 43
SESIP Assurance Levels & Protection Profiles
02
SESIP contribution for Automotive sector
Support for ISO/SAE 21434 Compliance:
SESIP's methodology supports compliance with ISO/SAE 21434, the international standard for automotive cybersecurity risk management.

## Slide 44
SESIP Assurance Levels & Protection Profiles
02
SESIP Assurance Levels
Adapt SESIP to your risk assessment:
SESIP levels let you tailor assurance to risk
Avoid overengineering: not every ECU needs SESIP 5
Enables scalable security investment based on product criticality
Fragmented and cost-sensitive automotive supply chain, SESIP offers flexibility.
For example, you can assign SESIP 2 for a temperature sensor, and SESIP 3 for a gateway that handles over-the-air (OTA) updates.
This ensures resources are focused where they yield the highest security value. The SESIP model supports iterative and modular certification, reducing total cost of ownership.

## Slide 45
SESIP Assurance Levels & Protection Profiles
02
SESIP Assurance Levels
Adapt SESIP to your risk assessment:
SESIP levels let you tailor assurance to risk
Avoid overengineering: not every ECU needs SESIP 5
Enables scalable security investment based on product criticality
Fragmented and cost-sensitive automotive supply chain, SESIP offers flexibility.
For example, you can assign SESIP 2 for a temperature sensor, and SESIP 3 for a gateway that handles over-the-air (OTA) updates.
This ensures resources are focused where they yield the highest security value. The SESIP model supports iterative and modular certification, reducing total cost of ownership.

## Slide 46
SESIP Assurance Levels & Protection Profiles
02
Why Protection Profiles Matter
Define security objectives and scope early
Enable harmonization across the supply chain
Lower certification cost
SESIP Protection Profiles

## Slide 47
SESIP Assurance Levels & Protection Profiles
02
Why Protection Profiles Matter
Define security objectives and scope early
Enable harmonization across the supply chain
Lower certification cost
SESIP Protection Profiles

## Slide 48
SESIP Assurance Levels & Protection Profiles
02
Continuous work to adapt to industry needs:
Technical working groups to standardize criteria and requirements
  Harmonize criteria for attacks (i.e., minimum/maximum attack scoring for specific attack scenarios)
  Harmonize acceptance on ad-hoc approaches (i.e., test witnessing in vendor facilities)
ITSEFs in alignment with certification bodies to adapt requirements to discuss ad-hoc approaches for specific use cases.
  Workshop to go though implementation instead of in-house code review
  Specific test-setups to facilities exposure of attack surface
  Alternative functional test methods to demonstrate compliance
GlobalPlatform role within the certification ecosystem

## Slide 49
Attack Potential & Attack Methods
01
A common and optimized approach for evaluating the security of connected products:
General model similar to CC
Granularity
Requirement hierarchy
Profiles
SESIP Assurance Levels and Protection Profiles

## Slide 50: Final thoughts
Context
Attack Potential & Attack Methods
SESIP Assurance Levels & Protection Profiles
Final thoughts

## Slide 51
Final thoughts
03
Key Takeaways
ENISA's Attack Potential Method:
Harmonized criteria to rate attack difficulty
SESIP Certification:
A common and optimized approach for evaluating the security of connected products